## Slide 1: Introduction to Pioneer 3-DX, ARIA and MobileSim

## Slide 2: What is Pioneer
Pioneer is a family of mobile robots, including two-wheel and four-wheel drive versions.
  http://www.mobilerobots.com/
Pioneer 3-AT
Pioneer 3-DX
Pioneer LX

## Slide 3: Pioneer 3-DX
Specifications
Side view
Top view
Control Panels

## Slide 4: Pioneer 3-DX
Sonars
  8 sonar arrays: One on each side, and six facing outward at 200 intervals
  Range from 10cm to 5m
Top
Front
0
1
2
3
4
5
6
7
Sonar numbers

## Slide 5: Connection Options
All MobileRobots platforms are served in a client-server architecture.

## Slide 6: ARIA
Open-source C++ library for all MobileRobots platforms and many accessory devices.
Applications developed with ARIA can easily navigate the mobile platform, as well as manage odometry, sensor readings, and other operating data.
Download link: https://reurl.cc/W4dl2x
Recommended OS: Ubuntu 16.04

## Slide 7: Examples of ARIA
Path
  /usr/local/Aria/examples
Important examples
  demo.cpp
    General purpose testing and demo program, using ArMode classes to provide keyboard control of various robot functions.
  wander.cpp
    Example using actions and sonars to implement a random wander avoiding obstacles.

## Slide 8: MobileSim
MobileSim provides a simulation environment for MobileRobots platforms and many accessories.
Download link: https://reurl.cc/Qpdzr5
The following pages show how to run MobileSim on Windows and Ubuntu.

## Slide 9: Ubuntu
Download ARIA and MobileSim.
  Latest Version for Ubuntu 16.04
    ARIA 2.9.4
    MobileSim 0.9.8
Install them with the file.
  They should be located at:
    /usr/local/Aria
    /usr/local/MobileSim
Make ARIA before use it.

## Slide 10: Ubuntu

## Slide 11: Ubuntu

## Slide 12: Ubuntu

## Slide 13: Assignment1 Announcement
Assignment1 is now live on CEIBA.
  Deadline: 2019/10/07 13:00
  Make sure you followed the requirements before submission.